## Slide 1: Terra-Audit
Institute of Information Technology
University of Dhaka
SE801 · SOFTWARE PROJECT LAB 3 · FINAL DEFENSE
AI-Assisted Digital MRV Platform for AWD Rice Irrigation and Agricultural Land Management Carbon Credits
PRESENTED BY
Kazi Nahid
BSSE Roll 1437
SUPERVISED BY
Dr. Emon Kumar Dey
Professor, IIT, DU
DATE
October 2026
Final defense
terra-audit.vercel.app
Signal analytics · Sentinel-1 AWD detection
Chart: 
| 09 Jan | 21 Jan | 02 Feb | 14 Feb | 26 Feb | 10 Mar | 22 Mar | 03 Apr | 15 Apr | 27 Apr | 09 May | 21 May
VV z-score (smoothed backscatter) | 1.023 | 0.441 | -0.14 | -0.942 | -1.44 | -0.111 | 0.39 | -0.606 | -1.326 | -0.083 | 0.857 | 1.936
Flood threshold (−0.8) | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8
Flooded | -0.942 | -1.44 | -1.326
AWD drydown | -0.111 | -0.083
2 AWD drydowns
→ 2.12 tCO₂e / ha
Verra VM0051 · VM0042
Notes: [0:15 · builds automatically] Good morning. I'm Kazi Nahid; my project is Terra-Audit — a platform that turns a rice field into an auditable carbon claim, with every number traceable to its evidence.

## Slide 2: Flooded rice emits methane — and AWD reductions are hard to prove
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
2
METHANE EMISSION FACTOR
1.00 → 0.55
Alternate Wetting & Drying (AWD) — draining the field at least twice per season — cuts the daily methane factor by 45% versus continuous flooding.
IPCC 2019 Table 5.12, used by Verra VM0051
Practice claims are hard to verify
Farmer irrigation logs are incomplete; sensors on every smallholder plot are too costly.
Evidence gets separated from the number
Spreadsheets lose the factors, methodology version and history behind a result.
Verification needs traceability
Verifiers and buyers must trace each tonne of CO₂e back to its evidence.
Notes: [0:35] Flooded paddies are a major methane source. AWD is a proven fix — the IPCC factor drops from 1.00 to 0.55. [click] The problem is MRV: proving the practice happened, and keeping the carbon number traceable to evidence.

## Slide 3: Terra-Audit links every carbon number to its evidence
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
3
An evidence-first digital MRV platform — from field boundary to reviewed export.
1
Register field
draw / upload boundary
2
Seasons & evidence
practices · files
3
Satellite analytics
background job
4
Readiness check
per requirement
5
Calculate & commit
frozen snapshot
6
Internal review
approve / changes
7
Export
PDF · JSON · CSV
Rice — Alternate Wetting & Drying
Verra VM0051 v1.1
Satellite-detected drydowns cut methane; 15% QA3 uncertainty and the N₂O penalty are deducted.
Agricultural Land Management
Verra VM0042 v2.2 + VMD0054 v1.1
Measured soil-carbon change plus N₂O, fire and fuel terms, minus leakage and a non-permanence buffer; missing leakage evidence blocks the result.
Notes: [0:40] One sentence: an evidence pipeline, not a black-box calculator. [click] Seven steps — the highlighted ones, satellite analytics and the calculation, are the two engines I'll open up next. [click] Two Verra methodologies implemented in deterministic code: rice AWD and agricultural land management.

## Slide 4: Sentinel-1 radar detects AWD drydowns without field sensors
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
4
Chart: 
| 09 Jan | 21 Jan | 02 Feb | 14 Feb | 26 Feb | 10 Mar | 22 Mar | 03 Apr | 15 Apr | 27 Apr | 09 May | 21 May
VV z-score (smoothed backscatter) | 1.023 | 0.441 | -0.14 | -0.942 | -1.44 | -0.111 | 0.39 | -0.606 | -1.326 | -0.083 | 0.857 | 1.936
Flood threshold (−0.8) | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8 | -0.8
Flooded | -0.942 | -1.44 | -1.326
AWD drydown | -0.111 | -0.083
Flooded
VV z-score below −0.8
Drydown
VV rises > 1.2σ right after a flooded date
Season
VH minimum = sowing; sharpest VH drop after the peak = harvest
Result fed to the calculation
2 AWD events · 84-day season
Live run on the deployed app · Sentinel-1 via Google Earth Engine · 12 observations, Jan–May 2026 · rule engine: AdaptiveAWDGate
Notes: [0:45] Radar sees through monsoon clouds. [click] The chart draws: flooded fields reflect less, so VV drops; when the field drains, VV jumps. [click] The three rules — below −0.8 is flooded; a jump right after a flooded date is a drydown; VH gives sowing and harvest. This live run found two drydowns and an 84-day season.

## Slide 5: Machine learning cross-checks the detector — but is not ground truth
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
5
Random Forest
predicted
dry
flooded
drydown
dry
19
2
1
flooded
2
8
1
drydown
2
1
0
75.0%
agreement
0.524
macro-F1
XGBoost
predicted
dry
flooded
drydown
dry
19
3
0
flooded
4
6
1
drydown
2
1
0
69.4%
agreement
0.460
macro-F1
Rows = threshold-gate label · 3-fold stratified cross-validation
Why add ML?
Rules are explainable but brittle. Models trained on the same Sentinel-1 features flag dates where the rules may be wrong.
Honest limitation
Models learn the gate's own labels, so this is agreement — not field accuracy. ML stays advisory until independent ground truth exists.
AI Validation page on the deployed app · features include vv_diff, vv_smoothed, vh, cross-ratio, days since sowing
Notes: [0:30] [click] Two models cross-check the rule engine: 75% and 69% agreement. [click] And I say upfront what this is not — there's no independent field ground truth yet, so these are agreement scores and ML stays advisory.

## Slide 6: A deterministic VM0051 engine turns evidence into tCO₂e
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
6
E = EFc × SFw × SFp × SFo × days × area
ΔCH₄ = Ebaseline − Eproject
ΔCO₂e = ΔCH₄ × 28 ÷ 1000
ER = ΔCO₂e × (1 − 15%) − PEN₂O
VM0051 Eq. 6–8, 29 (QA3) · EFc = 0.85 kg CH₄/ha/day (IPCC 2019, South Asia) · GWP CH₄ = 28 (AR5)
WATER-REGIME FACTOR SFw — WHERE AWD'S BENEFIT COMES FROM
1.00
Continuous flooding
0 drydowns
0.71
Single aeration
1 drydown
0.55
True AWD
≥ 2 drydowns
Worked example
1 ha · 84 days · 2 drydowns · 100 kg N/ha
Baseline CH₄
205.5 kg
Project CH₄
113.0 kg
Avoided CH₄
92.5 kg
As CO₂e
2.59 t
− 15% uncertainty
− 0.39 t
− N₂O penalty
− 0.08 t
Net reduction
2.12 tCO₂e
Above 60,000 tCO₂e/yr the engine blocks instead of guessing.
Worked example computed by CarbonAssetEngine.calculate_credits() (src/carbon/rice.py)
Notes: [0:45] Plain deterministic code, not AI. [click] The four lines appear in order: emissions, the difference, CO2e, and the net reduction. [click] The 0.55 factor — two or more drydowns — is where AWD's benefit comes from. [click] Worked example: one hectare, 84 days, two drydowns gives 2.12 tonnes CO2e, computed by the engine itself.

## Slide 7: Readiness gates never let an unsupported requirement pass silently
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
7
Readiness checklist — live run, VM0051 field
satisfied
common.monitoring_period_coverage
Crop seasons cover the monitoring period
needs review
common.methodology_applicability
Declared crop outside usual scope — reviewer confirms
needs review
common.evidence_review_status
Field observations not yet accepted by a second person
missing
vm0051.required_measurement_inputs
AWD events and season length not yet supplied
unsupported
vm0051.leakage_assessment
Not implemented — stays blocking
unsupported
common.additionality
Expert determination — never automated
1 satisfied
3 needs review
1 missing
4 unsupported
AT COMMIT, THE SYSTEM FREEZES
Field boundary & area
Crop seasons & engine inputs
Methodology bundle & factors
Readiness result
INTERNAL REVIEW
submitted
in_review
internally_approved
or changes requested / rejected / withdrawn
Live readiness run on the deployed app (6 of 9 checks shown) · internal approval is not VVB verification or Verra issuance
Notes: [0:40] [click] Every methodology requirement gets an explicit state. The bottom two — leakage and additionality — are unsupported and stay blocking: the system tells you what it cannot check. [click] At commit everything is frozen into a snapshot so the number is reproducible, then it goes through internal review.

## Slide 8: AI explains, code calculates, humans approve
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
8
AUTHORITATIVE · DETERMINISTIC
Project & evidence
Data validation
VM0051 / VM0042 engine
Results & readiness
ADVISORY · AI
Satellite, ML & crop models
Bundle-scoped context packet
LLM provider
Output validator
Draft explanation
Human reviewer
Bounded context
AI only sees the active methodology bundle, evidence and calculation.
Validated output
Citations must exist and numbers must match; “certified” or “approved” claims are rejected.
Fail closed
One retry, then fail — nothing partial is saved.
No AI component can change a calculated value, mark a requirement compliant, or create registry credits
Notes: [0:30] [click] The top lane is deterministic and authoritative — it owns every number. [click] The bottom lane is AI: bounded context, an LLM, and a validator; the output is only a draft for a human reviewer. [click] Three guardrails — test case TC-06 proves the validator.

## Slide 9: Layered components, deployed as web, API and worker
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
9
COMPONENT LAYERS
Next.js
Web app
API proxy
FastAPI
Routers & schemas
JWT · roles
Domain (src/)
Evidence
Methodology
Carbon
Signals & AI
Persistence
SQL · private files
Durable jobs
queue · worker
External
Earth Engine · LLMs
DEPLOYMENT
Browser
HTTPS
Vercel
Next.js 16 · React 19
Railway
Docker · FastAPI
Database
SQLite · PostgreSQL*
Evidence files
local · S3-compatible*
Python worker
durable job queue
Google Earth Engine
Sentinel-1
LLM providers
Groq / OpenAI-compatible
Solid = verified in the recorded run · dashed = configured external service · * supported hosted option
DESIGN EVOLUTION
midterm → final
Streamlit monolith → Next.js + FastAPI
Request-coupled jobs → Durable queue + worker
Scalar results → Versioned snapshots
Deployment as recorded in the final report (§5.5) · production worker and storage provenance not yet verified end to end
Notes: [0:35] [click] Three layers: Next.js talks to FastAPI through an authenticated proxy; FastAPI enforces roles; domain logic lives in shared components. [click] Deployed on Vercel and Railway, with a separate worker for long satellite and AI jobs. [click] And how it evolved from the midterm Streamlit prototype.

## Slide 10: Design classes, persistent data and behaviour
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
10
KEY DESIGN CLASSES & MODULES
AdaptiveAWDGate
analyze_irrigation_behavior()
extract_phenology()
SpatialDataEngine
extract_clean_timeseries()
Sentinel-1 via Earth Engine
CarbonAssetEngine
calculate_credits()
VM0051 rice AWD
AlmCarbonEngine
calculate_credits()
VM0042 + VMD0054 leakage
methodology.readiness
build_readiness_checklist()
per-requirement states
carbon.snapshot
build_snapshot()
calculate_from_snapshot()
WorkerContext · jobs
create_job()
claim_next_job()
AttachmentStorage
LocalFilesystemStorage
S3Storage (strategy)
PERSISTENT DATA (50+ TABLES)
Identity
organizations · users · project_members
Fields & evidence
fields · crop_seasons · practice_events · attachments
Methodology
methodology_bundles · methodology_requirements · readiness_determinations
Calculation & review
calculations · review_submissions · findings
Jobs & AI
background_jobs · workers · ai_records
BEHAVIOUR (STATE MACHINES)
Calculation version
draft
ready_for_review
decided by blocking readiness items
superseded
new evidence → new version
Background job
pending
running
done
or error (retry / invalid) · cancel_requested → cancelled · heartbeat-monitored workers
Names as in the source code (src/, backend/worker.py) · review states shown on the readiness slide · full ER model in the report (§4)
Notes: [0:40] Component-level design. [click] The key classes and modules with their main operations — each maps to one responsibility, and storage is a strategy: local filesystem or S3. [click] Over fifty tables, grouped by domain. [click] Behaviour: a calculation is draft or ready-for-review depending on blocking readiness items, and is superseded, never edited; jobs move pending → running → done, with cancellation and retries.

## Slide 11: Interface design: every user action has a visible state
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
11
Register a field
OBJECTS
map canvas · input-mode tabs
ACTION
draw / upload GeoJSON-KML / paste
STATE
boundary → confirm details → field saved
Signal analytics
OBJECTS
analysis window · detector · Run
EVENT
close < open → inline error
STATE
job pending → results + audit trail
Calculation & readiness
OBJECTS
seasons · period · Check readiness
EVENT
Check readiness → checklist
STATE
Commit → draft / ready_for_review
Shared labelled controls · inline validation · text + colour status cues · DD-MM-YYYY dates · keyboard-aware controls · responsive layouts
Notes: [0:35] Interface design as the user sees it. [click] Registering a field: three input modes, the map previews the boundary and area. [click] Signal analytics: validation is inline — here an invalid date range — and running the engine creates a background job. [click] Calculation: Check readiness renders the checklist; commit freezes a version.

## Slide 12: Code: the AWD rule engine produces an auditable trail
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
12
Date | VV z-score | Flooded | Drydown
09 Jan | 1.023 |  | 
21 Jan | 0.441 |  | 
02 Feb | -0.140 |  | 
14 Feb | -0.942 | ✓ | 
26 Feb | -1.440 | ✓ | 
10 Mar | -0.111 |  | ✓
22 Mar | 0.390 |  | 
03 Apr | -0.606 |  | 
15 Apr | -1.326 | ✓ | 
27 Apr | -0.083 |  | ✓
09 May | 0.857 |  | 
21 May | 1.936 |  | 
src/signals/threshold_gate.py · AdaptiveAWDGate (excerpt)
# Field-level statistical baseline
vv_mean = df["vv_smoothed"].mean()
vv_std = df["vv_smoothed"].std()
if vv_std == 0 or np.isnan(vv_std):
vv_std = 0.1 # Prevent division by zero on flat test data
# Z-score flood state detection
df["vv_zscore"] = (df["vv_smoothed"] - vv_mean) / vv_std
df["is_flooded"] = np.where(
df["vv_zscore"] < self.z_flood_threshold, 1, 0)
# Drydown event = sharp positive jump following a flooded state
df["vv_diff"] = df["vv_smoothed"].diff().fillna(0)
threshold_jump = self.dynamic_delta_sigma * vv_std
df["drydown_event"] = np.where(
(df["vv_diff"] > threshold_jump)
& (df["is_flooded"].shift(1) == 1), 1, 0)
Left: the columns this code produces, from the live run (audit-trail table in the app) · z_flood_threshold = −0.8, dynamic_delta_sigma = 1.2
Notes: [0:35 · no builds] Code review. Highlighted lines are the two rules. The table on the left is exactly what this code outputs for the live field — z-score, flooded flag and drydown flag — so a reviewer can verify each event by hand.

## Slide 13: Code: the credit engine blocks instead of guessing — and a test proves it
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
13
src/carbon/rice.py · calculate_credits() (condensed)
# Baseline vs project CH4 (Eq. 6/8)
e_baseline = self.ef_c * 1.0 * sc_p * sc_o_bsl * days * area_ha
e_project = self.ef_c * sf_w_project * sc_p * sc_o_wp * days * area_ha
delta_e_co2e = (e_baseline - e_project) * self.gwp_ch4 / 1000.0
# QA3 project-size gate (§8.6.3)
if delta_e_co2e > self.QA3_PROJECT_SIZE_GATE_TCO2E_YR:
return {"qa3_pathway_valid": False,
"final_issuance": None, ...}
# 15% uncertainty, N2O penalty (Eq. 25), net (Eq. 29)
ch4_after_unc = delta_e_co2e * (1 - self.UNC_QA3_DEFAULT)
pe_n2o = (self._n2o_irrigation_penalty(q_n, area_ha)
if awd_events > 0 else 0.0)
final_issuance = max(0.0, ch4_after_unc - pe_n2o)
tests/test_carbon_calculator.py
def test_qa3_project_size_gate_blocks_oversized_projects(
engine):
r = engine.calculate_credits(
awd_events=2, season_length_days=120,
area_ha=500_000.0, q_n_kg_per_ha=0.0)
assert r["qa3_pathway_valid"] is False
assert r["final_issuance"] is None
• Every factor is a named constant cited to its VM0051 / IPCC table
• All intermediate values are returned for the audit trail
• Snapshot calculation never re-reads the live database
Engine code condensed for the slide — full function in src/carbon/rice.py · test passes in the 177-test backend suite
Notes: [0:35 · no builds] The engine mirrors the equation slide. Highlighted: the QA3 gate — above 60,000 tonnes per year it returns None rather than a wrong number. On the right, the actual unit test proving it with a 500,000-hectare input.

## Slide 14: 177 backend tests pass — layered from equations to tenant isolation
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
14
177
backend tests
0 failed · pytest
4 / 4
frontend tests
npm test
✓
production build
next build
✓
type check
TypeScript
0
lint errors
ESLint
Unit / regression
equations · golden values · hard gates
API / integration
auth · tenant isolation · jobs · exports
Frontend
tests · types · lint · build
Operational
deployment · external services
Pass criterion
0 failures, no unjustified skips — and unsupported states must stay explicit, never silently satisfied.
Risks → contingency
No ground truth → ML advisory · unimplemented rules → blocking checks · live services → isolated fixtures.
All five checks re-run on the current code, 7–8 Oct 2026 · ESLint: 0 errors, 5 warnings
Notes: [0:30] 177 backend tests, zero failures — re-run this week — plus frontend tests, build, type check and lint. [click] Tests are layered so a green calculator can't hide a broken permission check. [click] Pass criteria and risks.

## Slide 15: Key test cases prove gates, isolation and reproducibility
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
15
ID | Scenario | Expected | Observed | Result
TC-01 | QA3 size gate — 500,000 ha field | Reject above 60,000 tCO₂e/yr | qa3_pathway_valid = False, no issuance | PASS
TC-03 | Another organization reads a field | Cannot list or open it | empty list · direct GET → 404 | PASS
TC-04 | PDF after live evidence is edited | Built from the frozen snapshot | owner 200 · viewer 403 · other org 404 | PASS
TC-06 | AI output claims “certified” | Reject; one retry, then fail | validation error · nothing saved | PASS
Evidence: tests/test_carbon_calculator.py · tests/backend/test_fields_endpoints.py · test_evidence_verification.py · tests/test_ai_validate.py
Notes: [0:30 · no builds] Four cases, one per risk: the calculator refuses an invalid pathway, tenants are isolated, exports stay reproducible after edits, and AI cannot claim certification. All pass in the suite.

## Slide 16: Challenges solved — and what remains
INTRODUCTION
SYSTEM
DESIGN
CODE & TESTS
REFLECTION
Terra-Audit · SE801 Final Presentation
16
CHALLENGE → SOLUTION
Methodology fidelity
Factors cited to tables + golden-value tests — caught a wrong EF (1.4 → 0.85).
Slow satellite & AI work
Durable job queue with a separate Python worker.
Numbers drifting after edits
Immutable snapshots; edits create a new version.
STILL OPEN
• Additionality unsupported (blocking)
• No independent AWD ground truth
• AI evaluation set incomplete
• Production provenance unverified
NEXT
• Field ground-truth campaign
• Eq. 38 uncertainty for large projects
• Remaining VM0051 terms
Software verification ≠ VVB verification ≠ Verra registration or issuance
Notes: [0:40] [click] Three hard problems and how I solved them — the emission-factor correction is the best story: code-level citations plus tests caught a value that inflated every result by about 1.65×. [click] Then state the limitations confidently — they are documented in the product itself, not hidden.

## Slide 17: Thank you
Questions are welcome
Live app terra-audit.vercel.app
Repository github.com/knah1d/terra-audit
Presenter Kazi Nahid · BSSE 1437
Supervisor Dr. Emon Kumar Dey, Professor, IIT, DU
Live app
GitHub
Notes: Leave this slide up during Q&A.